## Slide 2: Ponto Series
A complete solution to Control and Remote I/O

## Slide 3
Modular I/O system with field bus technology
Ponto Series
Direct connection of field wiring to the modules, without extra terminal blocks
Integrated fuses in the module

## Slide 4: Ponto Series
Remote connection to different PLCs using standard field buses
  Ethernet
  Profibus
  Modbus
  Devicenet

## Slide 5: Ponto Series
Direct connection to PCs / SoftPLCs
Different field bus communication protocols
  Ethernet
  Profibus
  Modbus
  Devicenet

## Slide 6: CPUs
Direct connection to the Ponto series I/O modules
Ethernet
Internet
Integrated control network
High connectivity CPUs with small size
WebPLC: Direct connection to Internet

## Slide 7: Ponto Module
Module
5
0
5
0
Base
Rail
Base
Module
PO1031
2
3
4
5
6
8
7
10
9
11
12
14
13
15
16
F
1
Label
Motor 1
Motor 2
Bomba 34 1
Rele Prot 456
Rele Prot 231
Motor 1
Motor 2
Bomba 34 1
Rele Prot 456
Rele Prot 231
Motor 1
Motor 2
Bomba 34 1
Rele Prot 456
Rele Prot 231
Motor 2
Modulo 1
5
0
5
0
PO1031
2
3
4
5
6
8
7
10
9
11
12
14
13
15
16
F
1
Field wiring
24
Field power supply

## Slide 8: Architecture
Power supply
I/O modules
Bus expansion
Local bus
Remote bus
CPU
Field bus heads

## Slide 9: Bus Capacities
Segment 0
Segment 1
Segment 2
Segment 3
10 modules max
4
Segments max
30 modules maximum total

## Slide 10: Ponto Base
Keyswitch with one code for each module type
Hot-swap modules without disturbing field wiring
Spring or barrier style terminals
Fuse option for any kind of module
Standard terminal identification
High connection density: 16 or 32 points in 10 cm

## Slide 11: GBL Bus
Automatic identification and addressing of the modules
Any module can be hot-swapped
12Mbaud serial bus, I/O scan time 0,45 ms for 480 points
Connection of 30 modules X 16 points = 480 points
Full hardware implementation with dedicated chips
12Mbaud

## Slide 12: Assembling Advantages

## Slide 13: Old panel...
Large quantities of wires between controller and terminal blocks
Costly identification
To many blocks per point
Complex power supply wiring
Bulky electrical project
Identification
Controller
Power supply
Identification
Terminal blocks
Field wiring
Supply wiring
Panel wiring
Supply wiring
Identification

## Slide 14: ... Ponto panel
No I/O terminal blocks and associated panel wiring
Panel size reduction
Big cost reduction of materials: Panel, Terminal Blocks, Wiring
Labor savings in the project and electric panel assembling
Big assembling time reduction !
Simpler commissioning
Point identification
Power supply
Field wiring
Controller

## Slide 15: Size reduction
20% smaller area
47% smaller depth
50% smaller volume
24
192 Points panel
1200
950
760
760
350
220
24

## Slide 16: Cost reduction
Simpler project
Smaller panel
No field terminal blocks
Big reduction of internal wiring
Significant assembling labor reduction
Cost reduction of more than 30% in the electrical panel

## Slide 17: CPUs

## Slide 18: PO3045 CPU
CPU
5
0
5
0
BAT
PO3044
E
BA
TX
RX
F
R
WebPLC
RX
RX
Ponto
5
0
5
0
PO1031
2
3
4
5
6
8
7
10
9
11
12
14
13
15
16
F
1
Modbus
Programmer interface
Ethernet TCP/IP
Serial interface 2

## Slide 19: High connectivity
Integrated Ethernet TCP/IP network
Ethernet TCP/IP
Internet
Http
FTP
SMTP
WebPLC : Integrated internet protocols for remote supervision and diagnostics
  Http ( browsers )
  FTP ( file transfers )
  SMTP ( e-mail )

## Slide 20: Web applications
Browser access to pages in the CPU
Complete remote diagnostics
e-mail of process alarm/events
Java applications
`C` language programming for special applications
Gateway for older equipment's

## Slide 21: PO3045 CPU
32bits microprocessor
4096 digital I/O points
512 analog I/O points
512kb user program memory
Integrated Ethernet TCP/IP network
WebPLC: Http, FTP, SMTP protocols
3 serial channels
Small dimensions

## Slide 22: ProPonto
Graphical bus configuration
Automatic configuration checking

## Slide 23: ProPonto
Tag allocation to I/O points
Module parameterization (ex: analog signal type )
Part list generation
Tag label printing for I/O modules
Read/write to I/O points for comissioning
Modules diagnostic

## Slide 24: Products

## Slide 25: Ponto Series products
PO 1000
PO 3xcc
Input modules
CPUs
PO 2xcc
Output modules
PO 4xcc
Field bus interfaces
PO 5xcc
Field bus heads
PO 1xcc
PO 1000
PO 8xcc
Bases
Power supply's and accessories
PO 7xcc
Special modules
PO 9xxx
Software
PO 6xxx

## Slide 26: Field Buses

## Slide 27: Field bus Heads
Field bus heads integrated with power supplies
Different protocols:
  Ethernet
  Devicenet
  Modbus
Redundant heads
Hot swap

## Slide 28: The ultimate

## Slide 29: Input modules
PO 1000
PO 1002
16 DI 24 Vdc opto
16 DI 220Vac opto
PO 1001
16 DI 110 Vac opto
PO 1003
16 DI 48 Vdc opto
PO 1112
8 AI isolated universal (V,I,Thermocouple, RTD, mV, R, NTC )
PO 1000
Module
Code
PO 1007
32 DI 24 Vdc opto
PO 1009
16 DI 24 Vdc opto com interrupção

## Slide 30: Output module
PO 1000
PO 2022
16 DO 24 Vdc / 2 A transistor opto
16 DO Relé 2 A NA dry contact
PO 2021
16 DO 110/220 Vac / 2 A triac opto
PO 2028
24 DO transistor
PO 2020
Module
Code
PO 2132
4 AO isolated

## Slide 31: CPU models
Ethernet network
Serial canal RS232 1
Memory
I/O modules
PO3042
No
Yes
256k
16
PO3043
No
Yes
256k
30
PO3044
Yes
Yes
512k
30
Clock
Yes
Yes
Yes
Web protocols
No
No
No
Serial canal RS232 2
Yes
Yes
Yes
Serial canal RS485 is.
No
Yes
Yes
PO3045
Yes
Yes
512k
30
Yes
Yes
Yes
Yes